## Slide 1: Three Level inverter
Rachakonda Shri Rama Akshay

## Slide 2: Why three level inverter
Better waveform quality than 2-level inverter
VRY = ± VDC, 0, ± 0.5VDC
R at +, Y at 0, gives 0.5VDC
R at 0, Y at - gives 0.5VDC
Level depends on number pole voltage, VRO= 0.5VDC , 0, - 0.5VDC
Three switches each leg required
sw2
Sw1 and sw3

## Slide 3: Switching State
Advantage: Reduced and harmonics in output AC voltages
DC input voltage of the inverter is spilt by two cascaded capacitors providing floating neutral point (load star point and DC link neutral are not connected).
Capacitors can be charged or discharged by inverter neutral current iz, causing DC link neutral voltage to vary.
This variation is the floating of the neutral point.
Main features 3- Level inverter
Switching State | S1 | S2 | S3 | S4 | Inverter Terminal Volt (AZ)
P | 1 | 1 | 0 | 0 | E
0 | 0 | 1 | 1 | 0 | 0
N | 0 | 0 | 1 | 1 | -E

## Slide 4: Switching Combinations
3 combination | voltge vector
PA,PB,PC | 0 voltage vector
OA,OB,OC | 
NA,NB,NC | 
Leg 1 Phase A |  |  |  |  | 
 | S1 | S2 | S3 | S4 | Vout
PA | 1 | 1 | 0 | 0 | Vd/2
OA | 0 | 1 | 1 | 0 | 0
NA | 0 | 0 | 1 | 1 | -Vd/2
Leg 2 Phase B |  |  |  |  | 
 | S1 | S2 | S3 | S4 | Vout
PB | 1 | 1 | 0 | 0 | Vd/2
OB | 0 | 1 | 1 | 0 | 0
NB | 0 | 0 | 1 | 1 | -Vd/2
Leg 3 Phase C |  |  |  |  | 
 | S1 | S2 | S3 | S4 | Vout
PC | 1 | 1 | 0 | 0 | Vd/2
OC | 0 | 1 | 1 | 0 | 0
NC | 0 | 0 | 1 | 1 | -Vd/2
Total Cases
PA can bewith PB, OB, or NB - 3 combination
1 case 3 choice , 3 case 9 combination
PC can be with those 9 combination
three c leg choices with 9 is total 27 combination

## Slide 5: Phase voltages as per Switching Combinations
 | Possible Switching Combinations |  |  | String Description (Vector symbol on the diagram) | Pole to Mid point Voltage |  |  | Common Mode Voltage | Phase Voltages |  |  | Clark Transform |  | Polar Transform |  | 
Combination No. | Ph A | Ph B | Ph C |  | Vao | Vbo | Vco | Vcm= (Vao+Vbo+Vco)/3 | Van | Vbn | Vcn | Vα | Vβ | ¦V¦ | θ | θ degree
1 | P | P | P | PPP | 0.5 | 0.5 | 0.5 | 0.500 | 0.000 | 0.000 | 0.000 | 0.00 | 0.00 | 0.00 | NA | NA
2 | O | O | O | OOO | 0 | 0 | 0 | 0.000 | 0.000 | 0.000 | 0.000 | 0.00 | 0.00 | 0.00 | NA | NA
3 | N | N | N | NNN | -0.5 | -0.5 | -0.5 | -0.500 | 0.000 | 0.000 | 0.000 | 0.00 | 0.00 | 0.00 | NA | NA
4 | O | O | P | OOP | 0 | 0 | 0.5 | 0.167 | -0.167 | -0.167 | 0.333 | -0.17 | -0.29 | 0.33 | 4.19 | 240
5 | N | N | O | NNO | -0.5 | -0.5 | 0 | -0.333 | -0.167 | -0.167 | 0.333 | -0.17 | -0.29 | 0.33 | 4.19 | 240
6 | P | O | P | POP | 0.5 | 0 | 0.5 | 0.333 | 0.167 | -0.333 | 0.167 | 0.17 | -0.29 | 0.33 | 5.24 | 300
7 | O | N | O | ONO | 0 | -0.5 | 0 | -0.167 | 0.167 | -0.333 | 0.167 | 0.17 | -0.29 | 0.33 | 5.24 | 300
8 | P | O | O | POO | 0.5 | 0 | 0 | 0.167 | 0.333 | -0.167 | -0.167 | 0.33 | 0.00 | 0.33 | 6.28 | 360
9 | O | N | N | ONN | 0 | -0.5 | -0.5 | -0.333 | 0.333 | -0.167 | -0.167 | 0.33 | 0.00 | 0.33 | 6.28 | 360
10 | P | P | O | PPO | 0.5 | 0.5 | 0 | 0.333 | 0.167 | 0.167 | -0.333 | 0.17 | 0.29 | 0.33 | 1.05 | 60
11 | O | O | N | OON | 0 | 0 | -0.5 | -0.167 | 0.167 | 0.167 | -0.333 | 0.17 | 0.29 | 0.33 | 1.05 | 60
12 | O | P | O | OPO | 0 | 0.5 | 0 | 0.167 | -0.167 | 0.333 | -0.167 | -0.17 | 0.29 | 0.33 | 2.09 | 120
13 | N | O | N | NON | -0.5 | 0 | -0.5 | -0.333 | -0.167 | 0.333 | -0.167 | -0.17 | 0.29 | 0.33 | 2.09 | 120
14 | O | P | P | OPP | 0 | 0.5 | 0.5 | 0.333 | -0.333 | 0.167 | 0.167 | -0.33 | 0.00 | 0.33 | 3.14 | 180
15 | N | O | O | NOO | -0.5 | 0 | 0 | -0.167 | -0.333 | 0.167 | 0.167 | -0.33 | 0.00 | 0.33 | 3.14 | 180
16 | N | O | P | NOP | -0.5 | 0 | 0.5 | 0.000 | -0.500 | 0.000 | 0.500 | -0.50 | -0.29 | 0.58 | 3.67 | 210
17 | O | N | P | ONP | 0 | -0.5 | 0.5 | 0.000 | 0.000 | -0.500 | 0.500 | 0.00 | -0.58 | 0.58 | 4.71 | 270
18 | P | N | O | PNO | 0.5 | -0.5 | 0 | 0.000 | 0.500 | -0.500 | 0.000 | 0.50 | -0.29 | 0.58 | 5.76 | 330
19 | P | O | N | PON | 0.5 | 0 | -0.5 | 0.000 | 0.500 | 0.000 | -0.500 | 0.50 | 0.29 | 0.58 | 0.52 | 30
20 | O | P | N | OPN | 0 | 0.5 | -0.5 | 0.000 | 0.000 | 0.500 | -0.500 | 0.00 | 0.58 | 0.58 | 1.57 | 90
21 | N | P | O | NPO | -0.5 | 0.5 | 0 | 0.000 | -0.500 | 0.500 | 0.000 | -0.50 | 0.29 | 0.58 | 2.62 | 150
22 | N | N | P | NNP | -0.5 | -0.5 | 0.5 | -0.167 | -0.333 | -0.333 | 0.667 | -0.33 | -0.58 | 0.67 | 4.19 | 240
23 | P | N | P | PNP | 0.5 | -0.5 | 0.5 | 0.167 | 0.333 | -0.667 | 0.333 | 0.33 | -0.58 | 0.67 | 5.24 | 300
24 | P | N | N | PNN | 0.5 | -0.5 | -0.5 | -0.167 | 0.667 | -0.333 | -0.333 | 0.67 | 0.00 | 0.67 | 6.28 | 360
25 | P | P | N | PPN | 0.5 | 0.5 | -0.5 | 0.167 | 0.333 | 0.333 | -0.667 | 0.33 | 0.58 | 0.67 | 1.05 | 60
26 | N | P | N | NPN | -0.5 | 0.5 | -0.5 | -0.167 | -0.333 | 0.667 | -0.333 | -0.33 | 0.58 | 0.67 | 2.09 | 120
27 | N | P | P | NPP | -0.5 | 0.5 | 0.5 | 0.167 | -0.667 | 0.333 | 0.333 | -0.67 | 0.00 | 0.67 | 3.14 | 180

## Slide 6: Condition for region selection
Conditions for Region Selection |  | 
s. no | Region | Condition
1 | Region 1 | m1 < 0.5
 |  | m2 < 0.5
 |  | m1+m2 <0.5
2 | Region 2 | m1 < 0.5
 |  | m2 < 0.5
 |  | m1+m2 > 0.5
3 | Region 3 | m1 > 0.5
4 | Region 4 | m2 > 0.5
)
)

## Slide 7: Hard Switching
 |  |  | Ta | Tb | Tc
Sector 1 | Region 1 | S1R1 | V1 | V0 | V2
 | Region 2 | S1R2 | V1 | V7 | V2
 | Region 3 | S1R3 | V1 | V7 | V13
 | Region 4 | S1R4 | V14 | V7 | V2
Sector 2 | Region 1 | S2R1 | V2 | V0 | V3
 | Region 2 | S2R2 | V2 | V8 | V3
 | Region 3 | S2R3 | V2 | V8 | V14
 | Region 4 | S2R4 | V15 | V8 | V3
Sector 3 | Region 1 | S3R1 | V3 | V0 | V4
 | Region 2 | S3R2 | V3 | V9 | V4
 | Region 3 | S3R3 | V3 | V9 | V15
 | Region 4 | S3R4 | V16 | V9 | V4
Sector 4 | Region 1 | S4R1 | V4 | V0 | V5
 | Region 2 | S4R2 | V4 | V10 | V5
 | Region 3 | S4R3 | V4 | V10 | V16
 | Region 4 | S4R4 | V17 | V10 | V5
Sector 5 | Region 1 | S5R1 | V5 | V0 | V6
 | Region 2 | S5R2 | V5 | V11 | V6
 | Region 3 | S5R3 | V5 | V11 | V17
 | Region 4 | S5R4 | V18 | V11 | V6
Sector 6 | Region 1 | S6R1 | V6 | V0 | V1
 | Region 2 | S6R2 | V6 | V12 | V1
 | Region 3 | S6R3 | V6 | V12 | V18
 | Region 4 | S6R4 | V13 | V12 | V1

## Slide 8: Hard Switching
 |  |  | Ta | Tb | Tc
Sector 1 | Region 1 | S1R1 | V1 | V0 | V2
 | Region 2 | S1R2 | V1 | V7 | V2
 | Region 3 | S1R3 | V1 | V7 | V13
 | Region 4 | S1R4 | V14 | V7 | V2
Sector 2 | Region 1 | S2R1 | V2 | V0 | V3
 | Region 2 | S2R2 | V2 | V8 | V3
 | Region 3 | S2R3 | V2 | V8 | V14
 | Region 4 | S2R4 | V15 | V8 | V3
Sector 3 | Region 1 | S3R1 | V3 | V0 | V4
 | Region 2 | S3R2 | V3 | V9 | V4
 | Region 3 | S3R3 | V3 | V9 | V15
 | Region 4 | S3R4 | V16 | V9 | V4
Sector 4 | Region 1 | S4R1 | V4 | V0 | V5
 | Region 2 | S4R2 | V4 | V10 | V5
 | Region 3 | S4R3 | V4 | V10 | V16
 | Region 4 | S4R4 | V17 | V10 | V5
Sector 5 | Region 1 | S5R1 | V5 | V0 | V6
 | Region 2 | S5R2 | V5 | V11 | V6
 | Region 3 | S5R3 | V5 | V11 | V17
 | Region 4 | S5R4 | V18 | V11 | V6
Sector 6 | Region 1 | S6R1 | V6 | V0 | V1
 | Region 2 | S6R2 | V6 | V12 | V1
 | Region 3 | S6R3 | V6 | V12 | V18
 | Region 4 | S6R4 | V13 | V12 | V1
Region 1
Region 2
Region 3
Region 4
N= 0 to 5

## Slide 9: Switching design requirements
 | Requirement of switching sequence design
1 | Transition from one switching state to another switching state requires operation of two switches within same leg
 | One switch turns On, another Turns Off
2 | Transition of Vref from one region or sector to another must take minimum switching
 | Effect of Switching states on Vz Voltage deviaiton |  | 
1 | O states [PPP,OOO,NNN] | Z is disconnected no change | 
2 | POO | iz current flows into Z point, voltge increases | 
3 | ONN | iz current flows out of Z point, voltge decreases | 
4 | PON | A phsae +ve, B phase 0 volt, C phase - ve | the current to Z point depends on the inverter - network condition
5 | PNN | Phases are connected between +ve and -ve and Z point is diconnected so no impact on neutral volt | 

## Slide 10: Subregion Selection for Minimum Voltage deviation
Sector 1 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S1R1a | V1P(POO) | V0(OOO) | V2N(OON) | V1b; | V2N(OON) | V0(OOO) | V1P(POO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S1R1b | V2N(OON) | V0(OOO) | V1P(POO) | V2P(PPO) | V1P(POO) | V0(OOO) | V2N(OON)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S1R2a | V1P(POO) | V7(PON) | V2N(OON) | V1N(ONN) | V2N(OON) | V7(PON) | V1P(POO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S1R2b | V2N(OON) | V7(PON) | V1P(POO) | V2P(PPO) | V1P(POO) | V7(PON) | V2N(OON)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S1R3 | V1P(POO) | V7(PON) | V13(PNN) | V1N(ONN) | V13(PNN) | V7(PON) | V1P(POO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S1R4 | V2N(OON) | V7(PON) | V14(PPN) | V2P(PPO) | V14(PPN) | V7(PON) | V2N(OON)
Sector 2 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S2R1a | V2N(OON) | V0(OOO) | V3P(OPO) | V2P(PPO) | V3P(OPO) | V0(OOO) | V2N(OON)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S2R1b | V3P(OPO) | V0(OOO) | V2N(OON) | V3N(NON) | V2N(OON) | V0(OOO) | V3P(OPO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S2R2a | V2N(OON) | V8(OPN) | V3P(OPO) | V2P(PPO) | V3P(OPO) | V8(OPN) | V2N(OON)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S2R2b | V3P(OPO) | V8(OPN) | V2N(OON) | V3N(NON) | V2N(OON) | V8(OPN) | V3P(OPO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S2R3 | V2N(OON) | V8(OPN) | V14(PPN) | V2P(PPO) | V14(PPN) | V8(OPN) | V2N(OON)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S2R4 | V3P(OPO) | V8(OPN) | V15(NPN) | V3N(NON) | V15(NPN) | V8(OPN) | V3P(OPO)

## Slide 11: Subregion Selection for Minimum Voltage deviation
Sector 3 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S3R1a | V3P(OPO) | V0(OOO) | V4N(NOO) | V3N(NON) | V4N(NOO) | V0(OOO) | V3P(OPO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S3R1b | V4N(NOO) | V0(OOO) | V3P(OPO) | V4P(OPP) | V3P(OPO) | V0(OOO) | V4N(NOO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S3R2a | V3P(OPO) | V9(NPO) | V4N(NOO) | V3N(NON) | V4N(NOO) | V9(NPO) | V3P(OPO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S3R2b | V4N(NOO) | V9(NPO) | V3P(OPO) | V4P(OPP) | V3P(OPO) | V9(NPO) | V4N(NOO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S3R3 | V3P(OPO) | V9(NPO) | V15(NPN) | V3N(NON) | V15(NPN) | V9(NPO) | V3P(OPO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S3R4 | V4N(NOO) | V9(NPO) | V16(NPP) | V4P(OPP) | V16(NPP) | V9(NPO) | V4N(NOO)
Sector 4 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S4R1a | V4N(NOO) | V0(OOO) | V5P(OOP) | V4P(OPP) | V5P(OOP) | V0(OOO) | V4N(NOO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S4R1b | V5P(OOP) | V0(OOO) | V4N(NOO) | V5N(NNO) | V4N(NOO) | V0(OOO) | V5P(OOP)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S4R2a | V4N(NOO) | V10(NOP) | V5P(OOP) | V4P(OPP) | V5P(OOP) | V10(NOP) | V4N(NOO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S4R2b | V5P(OOP) | V10(NOP) | V4N(NOO) | V5N(NNO) | V4N(NOO) | V10(NOP) | V5P(OOP)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S4R3 | V4N(NOO) | V10(NOP) | V16(NPP) | V4P(OPP) | V16(NPP) | V10(NOP) | V4N(NOO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S4R4 | V5P(OOP) | V10(NOP) | V17(NNP) | V5N(NNO) | V17(NNP) | V10(NOP) | V5P(OOP)
Sector 5 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S5R1a | V5P(OOP) | V0(OOO) | V6N(ONO) | V5N(NNO) | V6N(ONO) | V0(OOO) | V5P(OOP)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S5R1b | V6N(ONO) | V0(OOO) | V5P(OOP) | V6P(POP) | V5P(OOP) | V0(OOO) | V6N(ONO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S5R2a | V5P(OOP) | V11(ONP) | V6N(ONO) | V5N(NNO) | V6N(ONO) | V11(ONP) | V5P(OOP)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S5R2b | V6N(ONO) | V11(ONP) | V5P(OOP) | V6P(POP) | V5P(OOP) | V11(ONP) | V6N(ONO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S5R3 | V5P(OOP) | V11(ONP) | V17(NNP) | V5N(NNO) | V17(NNP) | V11(ONP) | V5P(OOP)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S5R4 | V6N(ONO) | V11(ONP) | V18(PNP) | V6P(POP) | V18(PNP) | V11(ONP) | V6N(ONO)
Sector 6 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S6R1a | V6N(ONO) | V0(OOO) | V1P(POO) | V6P(POP) | V1P(POO) | V0(OOO) | V6N(ONO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S6R1b | V1P(POO) | V0(OOO) | V6N(ONO) | V1N(ONN) | V6N(ONO) | V0(OOO) | V1P(POO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S6R2a | V6N(ONO) | V12(PNO) | V1P(POO) | V6P(POP) | V1P(POO) | V12(PNO) | V6N(ONO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S6R2b | V1P(POO) | V12(PNO) | V6N(ONO) | V1N(ONN) | V6N(ONO) | V12(PNO) | V1P(POO)
 |  | Ta/4 | Tb/2 | Tc/2 | Ta/2 | Tc/2 | Tb/2 | Ta/4
 | S6R3 | V6N(ONO) | V12(PNO) | V18(PNP) | V6P(POP) | V18(PNP) | V12(PNO) | V6N(ONO)
 |  | Tc/4 | Tb/2 | Ta/2 | Tc/2 | Ta/2 | Tb/2 | Tc/4
 | S6R4 | V1P(POO) | V12(PNO) | V13(PNN) | V1N(ONN) | V13(PNN) | V12(PNO) | V1P(POO)

## Slide 12: Parameters
Vd | 400 | V
Fsw | 900 | Hz
Fref | 50 | Hz
Pphase | 1 | kW
Qphase | 0.484 | kVAr

## Slide 13: Results

## Slide 14: Results